*** THE 'X:' DEVICE ***

*************************************
*                                   *
*  CHANGE NOTES:  fixes and mods    *
*                                   *
*   01/01/85   Calls to ATARI FP    *
*              ROM replaced with    *
*              integer math code    *
*                                   *
*   11/13/84  1. now supports BASIC *
*                PRINT statement    *
*             2. supports SYSTEM    *
*                RESET key properly *
*             3. some memory use    *
*                bugs fixed - now   *
*                can CLOSE/OPEN     *
*                repeatedly without *
*                using more memory  *
*                                   *
*************************************

The 'X' device driver is an 80-column
display device driver for all ATARI
computers. When loaded into memory it
installs itself between addresses
$2B00 and $35D0. Since it is not yet
relocatable this places it high 
enough to allow room for normal DOS
users (DOS/XL, OS/A+, DOS2.0s) and 
leaves space for the 'R' handler if
the 850 Interface Module is used. A
relocatable version is planned for
the future.

The 'X' device driver loads an 'X'
device entry in the Handler Address
Table and provides standard CIO 
interfacing to the driver, with some
caveats. When opened for OUTPUT it
performs like the 'E' device; all
usual cursor and editing controls are
followed and inverse video is
provided. When opened for UPDATE it
does not edit out cursor control
characters like the 'E' device, but
passes them back to the caller like
the 'S' device.

The 'X' device driver provides some
editing features that are not offered
by the 'E' or 'S' devices. ERASE Line
and Screen to and from the current
CURSOR position are provided via XIO
commands. Absoulte Cursor Positioning
is also provided via an XIO command.

            COMMANDS

OPEN #n,4,0,"X:"  - open #n using 'X'
CLOSE, GET, PUT   - as usual

XIO cmdno,#n,0,0,'X:'  - special cmds
 cmdno = $10 - position aux1,aux2
 cmdno = $20 - erase line to CURSOR
 cmdno = $21 - erase line fm CURSOR
 cmdno = $22 - erase screen to CURSOR
 cmdno = $23 - erase screen fm CURSOR

              USAGE

ATARI DOS users should name the 
XDSPLY file AUTORUN.SYS on their boot
disk. It can be concatenated to an
existing AUTORUN.SYS file, such as
the RS232 handler. OSS DOS/XL or 
OS/A+ users can leave the file as
a .COM file and install it by running
it like any other Extrinsic command.

              CAVEATS

XDSPLY does not replace the 'E:'
device. It can be used like it in
certain circumstances and you can
modify the OS's Handler Address Table
to substitute 'X:' for 'E:'; but not
all of the 'E:' features such as full
screen editing are supported.
               BUGS

Please report any bugs to me via
EMAIL on Compuserve at 70545,507
and I'll try to address them in the
next release.

Alex M. Stevens
70545,507



DL 3: